MS Project Proposal
Integrating A Category-Partition Testing Tool With A Combinatorial Interaction Testing Tool To Product T-Way Adequate Test Frames
Andrew Graff
[Speaker Notes: Add numbers to all slides There is Boise State templates – you might want to use those.]

---
Overview
Introduction
Objective of the project
Background on category partition method
  - TSL tool
Background on combinatorial interaction testing
  - CASA tool
Demo
Remaining work and timeline

---
Introduction
Testing is necessary to reduce faults in software.
Black box testing helps to find functional faults.
  - Category partition method allows for systematic design of test inputs software (TSL tool)
    - +Specification language translated into easy to run test frames
    - - All possible inputs add up quickly which is costly in execution time.
  - Combinatorial interaction testing select a subset of test cases that t-way adequate (CASA tool)
    - +Can reduce the number of test frames to a manageable level.
    - - Not user-friendly interface
[Speaker Notes: Make a case somewhere that with TSL we can make less test cases by reducing categories or collapsing some values of a category together. For example, for an integer input instead of have positive, zero and negative choices, we reduce it no zero and non-zero. With such approach we coarsen the test suite. While CASA allows us to stay at the same granularity level, but still give us a smaller test suite due to t-way coverage optimization.]

---
Objective of the project
Combine the user-friendly input/output interface of TSL with the powerful test case optimization algorithm of CASA
  1. TSL a tool that uses category partitioning to generate test frames
  1. CASA a tool that uses the combinatorial interaction method known as simulated annealing
[Speaker Notes: A bit better formating]

---
TSL
Testing Specification Language (TSL) – a good front-end interface for category partition method.
Create a single .tsl file that describes the categories and choices within those categories.
Generates all possible test frames with each category as an input.

---
TSL – example input
Software under test: ‘Tabs’ options in a browser
Create tabs.tsl to formally specify the categories and choices

---
TSL – example output

---
CASA
Covering Arrays by Simulated Annealing (CASA) – tool that implements the combinatorial interaction method of simulated annealing.
It can find t-way combinations of inputs to reduce the overall number of test frames required.
Programming the input is complicated.
[Speaker Notes: I am afraid that t-way combination is not clear here. Can you give a simple example: 3 categories and each has 2 choice. I think we had something like that: OS: Mac, Windows, Unix; Web browser: Chrome, Firefox; Processors: Intel, AMD The show 2-way (pairwise) result vs exhaustive result. Without such example it will not click for the committee.]

---
CASA – example input
.citmodel file
.contraints file
2 rules
2-way interaction
3 terms in this conjunctive clause
6 categories
If 3, then 5 or 6
# of choices
per category
2 terms in this conjunctive clause
If 4, then 7
*The numbers in the .constraints file will map back to
the choices from the original tsl input
[Speaker Notes: I like this slide very much!]

---
Demo
Do you think I should record and explain or do a live demo?
[Speaker Notes: Do a live demo – it should not take long time or requires elaborate connections to some servers. Everything runs local. Just to make sure have all the windows open for demo.]